| Insulation | Insulation Attachment | Membrane |
| --- | --- | --- |
| 30 year | I.S.O. 95+ GL Tapered I.S.O. 95+ GL Dens Deck (4) Dens Deck Prime (4) HailGard (8) | 30 year | Polymer Fasteners Firestone ISO Twin Pack (2) Firestone ISO Spray Adhesive(2) Firestone ISO-FIX Adhesive (2, 3) | 30 year | RubberGard Platinum .090 |
| 20 year | I.S.O. 95+ GL Tapered I.S.O. 95+ GL Dens Deck (4,5) Dens Deck Prime (4,5) HailGard (5,8) | 20 year | Polymer Fasteners Firestone ISO Twin Pack (2) Firestone ISO Spray Adhesive(2) Firestone ISO-FIX Adhesive (2, 3) Loose Laid (7) | 20 year | RubberGard Non Reinforced .060 (1) RubberGard Non Reinforced FR .060 (1) RubberGard Non Reinforced LSFR .060 (1) RubberGard MAX .060 or .045 (1) RubberGard MAX FR .060 or .045 (1) RubberGard MAX PT .060 or .045 (1) RubberGard Platinum .090 (1) |
| 15 year and less | I.S.O. 95+ GL Tapered I.S.O. 95+ GL Dens Deck (4,5) Dens Deck Prime (4,5) FiberTop Woodfiber FiberTop Woodfiber Composite HailGard (5,8) | 15 year recover | Polymer Fasteners Firestone ISO Twin Pack (2) Firestone ISO Spray Adhesive(2) Firestone ISO-FIX Adhesive (2, 3) Loose Laid (7) | 15 year and less | RubberGard Non Reinforced .060 or .045 (1) RubberGard Non Reinforced FR .060 or .045 (1) RubberGard Non Reinforced LSFR .060 or .045 (1) RubberGard MAX .060 or .045 (1) RubberGard MAX FR .060 or .045 (1) RubberGard MAX PT .060 or .045 (1) RubberGard Platinum .090 (1) |
|  |  | 15 year and less | Polymer Fasteners Firestone ISO Twin Pack (2) Firestone ISO Spray Adhesive(2) Firestone ISO-FIX Adhesive (2, 3) Loose Laid (7) |  |  |
| Notes: |
| Footnotes: The new roof membrane can be directly adhered to a Structural Concrete deck, New Cover Board, new insulation, or a combination of the above. See the Firestone Technical Database for specific installation requirements. Max Size Insulation Board 4’x4’. 3. Pull Test required on deck if ISO-FIX Adhesive is used to attach Insulation to deck. 4. Acceptable for use in 4’x8’ attachment with Twin Pack Adhesive 5. Not acceptable for top layer of insulation in Ballasted assembly. 6. Ballasted or Mechanically Attached Systems are not acceptable for 30 year warranties. 7. Loose laid insulation is only acceptable in Ballasted assemblies. 8. HailGard Insulation can only be installed using Firestone Polymer Fasteners. Building Height Limitations: Refer to the Firestone Technical Database for Building Height limitations for Firestone Adhered and Mechanically Attached Systems Base Tie-Ins: Must be constructed using the QuickSeam RPF Strip. | Slope Requirements: Minimum 1/8” slope recommended to promote positive drainage. Firestone Recommends a minimum of ¼” slope. Use of Air Barrier: An air barrier is required for projects with large openings that are greater than 10% of the total wall area that can be left open in a storm. Criteria to be determined based upon Firestone’s Review. Seam Construction: Side Laps and End Laps: Minimum 3” QuickSeam Splice Tape with QuickSeam Joint Covers at all “T” joints and wall intersections. Platinum systems require a double strip in of the seams utilizing 5” and 9” QuickSeam Flashing. Sheet Metal: Firestone Metal Edge System (Required for 30 year Platinum Warranty) Shop Fabricated pre-finished G-90 Galvanized Steel, Stainless Steel, Anodized or Extruded Aluminum. Other Requirements: As-Built projects not permitted. Firestone requires a Pre-Installation Notice 14 days prior to project installation. System installation per Firestone Technical Database. The Firestone Warranty does not cover products not supplied by Firestone Building Products |

# Text boxes

Sample Assembly

# Gypsum/Tectum Deck Specifications

# Adhered / Ballasted (6) / Mechanically Attached (6) RubberGard EPDM