EVERCLEAR VOX

Non-Yellowing, Low VOC, Water-Base Sealer

EVERCLEAR VOX is a water based pure acrylic sealer for concrete with excellent blush resistance and total resistance to yellowing from UV exposure.

{Note to Specifier: The paragraphs below are meant to be incorporated into Parts 2 and 3 of a standard CSI 3 Part Format specification, the General Structural Notes, or directly onto the plans. They must be carefully reviewed and edited to meet the requirements of the project and governing building codes. Coordinate with other specification sections and drawings.}

PART 2:	PRODUCT

2.__	CURING AND SEALING COMPOUND

A.	Concrete sealing compound. A ready-to-use, water-based acrylic sealing compound for use on existing, interior and exterior, horizontal and vertical concrete surfaces. Product shall conform to:

ASTM C 309, Type 1 Class A & B.

1. 	Product:

- Euclid Chemical Company (The); EverClear VOX www.euclidchemical.com

2.__	Manufacturer shall have ISO 9001 Quality Certification. To ensure compatibility all products shall be from the same manufacturer.

PART 3: 	EXECUTION

3.__ 	EXAMINATION

A. 	When used on existing concrete, examine concrete surfaces to receive curing and sealing compound. Notify specifier if surfaces are not acceptable. Do not begin surface preparation or application until unacceptable conditions are corrected.

3.__	 SURFACE PREPARATION

A. 	When used on existing concrete, prepare concrete surfaces in accordance with manufacturer’s written instructions.

B. 	Ensure surfaces are clean and free of standing water.

C. 	Remove dirt, dust, oil, grease, sealers, and other materials that may prevent adhesion of sealing compound.

3.__ 	APPLICATION

A. 	Do not apply to concrete to receive toppings, epoxy coatings, urethane coatings, or epoxy adhesives.

B. 	Do not use as a bond breaker for tilt-up construction.

C. 	Do not dilute sealing compound.

D. 	Cure concrete surfaces as specified in Section 03300.