### MATERIAL SAFETY DATA SHEET

4 = EXTREME

3 = HIGH

2 = MODERATE

1 = SLIGHT

0 = INSIGNIFICANT

GAF MATERIALS CORPORATION

TRIPLY(  ASPHALT/CONCRETE PRIMER

|  | CEMENTS AND COATINGS |
| --- | --- |
| Manufacturer: GAF MATERIALS CORP. | Identity (Trade Name As Used On Label): |
| Address 1361 ALPS ROAD | MSDS Number* 1014-U2 |
| WAYNE, NJ 07470 | CAS Number* N/A – Mixture |
| Phone Number (For Information) 800-766-3411 | Date Prepared 02/00 Rev. 05/03 |
| Emergency Phone Number 800-424-9300 | Prepared By* M. DISTEFANO |

NOTE: Blank spaces are not permitted. If any item is not applicable, or

no information is available, the space must be marked to indicate that.

| SECTION 1 - MATERIAL IDENTIFICATION AND INFORMATION |  |
| --- | --- |

| COMPONENTS - Chemical Name & Common |  | OSHA | ACGIH | OTHER LIMITS |
| --- | --- | --- | --- | --- |
| Names (Hazardous Components 1% or Greater; | %* | PEL | TLV | RECOMMENDED |
| Carcinogens 0.1% or greater) |  |  |  |  |
| Asphalt Base CAS #8052-42-4 | <60% |  | 0.5mg/M3 | Ceiling of 10mg/M3 |
| Volatile Petroleum Solvents | <40% | 100ppm | 350mg/M3 | Max. ( hr. 1,800mg/M3 |

| Non-Hazardous Ingredients |  |  |
| --- | --- | --- |
| Total | 100 |  |

| SECTION 2 - PHYSICAL/CHEMICAL CHARACTERISTICS |  |
| --- | --- |

| Boiling Point | 313°F | Specific Gravity (H2O = 1) | >1.0 |
| --- | --- | --- | --- |
| Vapor Pressure (mm Hg and Temperature) | ND | Melting Point | ND |
| Vapor Density (Air = 1) | ND | Evaporation Rate (Butyl Acetate = 1) | ND |
| Solubility in Water | Insoluble | Water Reactive | None |

Appearance and Odor: Dark color, viscous liquid, petroleum odor.

SECTION 3 - FIRE AND EXPLOSION HAZARD DATA

| Flash Point and >100°F Method Used NFPA | Auto-Ignition >400°F Temperature | Flammability Limits in Air % by Volume | LEL 0.9% | UEL 6.0% |
| --- | --- | --- | --- | --- |

Extinguisher Media: Dry Chemical, foam, water fog

Unusual Fire and Explosion Hazards: Petroleum-based compounds can float in water

*  Optional        ND = Not Determined	OSHA 174                                                                     Page 1/2

MSDS GAF

SECTION 4 – REACTIVITY HAZARD DATA

| STABILITY | Stable __x_ | Conditions |
| --- | --- | --- |
|  | Unstable ____ | To Avoid Keep from heat, sparks, open flame. |

Incompatibility (Materials to Avoid): Acids, caustics, chlorinated hydrocarbons, oxidizers

Hazardous Decomposition Products: Nitrogen oxides, carbon oxides

| HAZARDOUS POLYMERIZATION | Conditions |
| --- | --- |
| ___ May Occur _x___ Will Not Occur | To Avoid: N/A |

SECTION 5 - HEALTH HAZARD DATA

| PRIMARY ROUTES OF ENTRY: | CARCINOGEN LISTED IN: |
| --- | --- |
| _x_ Inhalation x_ Skin Absorption x_ Ingestion ___ Not Haz Vapors Very slight Slight | ___ NTP ___ IARC Monograph ___ OSHA __x_ Not Listed |

| HEALTH | Acute: Itching, unconsciousness, dizzy, dry skin, nausea |
| --- | --- |
| HAZARDS | Chronic: Difficult breathing (cancer studies - no friable fibers) |

Signs and Symptoms of Exposure: Repeated/continuous exposure can cause: chemical pneumonia, liver/kidney damage

Medical Conditions Generally Aggravated by Exposure: Repeated/continuous exposure can aggravate emphysema

EMERGENCY FIRST AID PROCEDURES - Large amounts may need immediate emergency treatment

Eye Contact: Flush eyes for 15 minutes with clean water, GET medical attention.

Skin Contact: Wash with soap and water. Get medical care if irritation persists.

Inhalation: Get to fresh air, administer oxygen or artificial respiration, seek medical attention

Ingestion: DO NOT INDUCE VOMITING, GET MEDICAL ATTENTION QUICKLY

SECTION 6 – CONTROL AND PROTECTIVE MEASURES

Respiratory Protection (Specify Type): Organic vapor cartridge if in an enclosed area

| Protective Gloves: Impervious to solvents | Eye Protection |
| --- | --- |
|  | Chemical goggles for vapors |

| VENTILATION | ___x_ Local Exhaust: If outside | __x__ Mechanical (General): If inside |
| --- | --- | --- |

| TO BE USED | __ __ Special: | _x___ Other (Specify): Avoid vapor concentrations |
| --- | --- | --- |

Other Protective Clothing and Equipment: Long sleeve shirt and long pants preferred.

Hygienic Work Practices: Wear gloves and eye goggles to prevent irritations.

SECTION 7 – PRECAUTIONS FOR SAFE HANDLING AND USE/LEAK PROCEDURES

Steps to be Taken if Material is Spilled or Released: Use non-sparking tools with absorbent material (limestone), shovel up and place in closed container for proper disposal

Waste Disposal Methods: RCRA regulated material. Consult local, state, and federal regulation for permitted land fill disposal or incineration.

Precautions to be Taken in Handling and Storage: Use in well-ventilated area, store in DRY, cool area

Other Precautions and/or Special Hazards: DO NO HEAT FOR APPLICATION. Wash contaminated clothing.

MSDS NO.  1014-U2                                                                                                                               PAGE 2/2