## MATERIAL SAFETY DATA SHEET

4 = EXTREME

3 = HIGH

2 = MODERATE

1 = SLIGHT

0 = INSIGNIFICANT

GAF MATERIALS CORPORATION

# TRIPLY(  MODIFIED BITUMEN ADHESIVE;

TRIPLY(  MODIFIED BITUMEN FLASHING CEMENT

|  | CEMENTS & COATINGS |
| --- | --- |
| Manufacturer: GAF MATERIALS CORP. | Identity (Trade Name As Used On Label) |
| Address 1361 ALPS ROAD | MSDS Number* 1014-U1 |
| WAYNE, NJ 07470 | CAS Number* |
| Phone Number (For Information) 800-766-3411 | Date Prepared 02/00 Rev. 06/03 |
| Emergency Phone Number 800-424-9300 | Prepared By* M. DISTEFANO |
| NOTE: Blank spaces are not permitted. If any item is not applicable, or |
| no information is available, the space must be marked to indicate that. |
| SECTION 1 - MATERIAL IDENTIFICATION AND INFORMATION |  |
| COMPONENTS - Chemical Name & Common |  | OSHA | ACGIH | OTHER LIMITS |
| Names (Hazardous Components 1% or Greater; | %* | PEL | TLV | RECOMMENDED |
| Carcinogens 0.1% or greater) |  |  |  |  |
| PETROLEUM DISTILLATE CAS# 8052-41-3 |  |  | 100 ppm 2 mm Hg @68o F | 50 |
| ASPHALT CAS# 8052-42-4 |  |  | 0.5 mg/M3 |  |
| PETROLEUM DISTILLATE CAS# 64742-95-6 |  |  |  | 50 ppm (245 mg/M3 ) for an 8 hr workday |
| There are no SARA ingredients in this material in excess of deminimum amounts |  |  |  |  |
| SECTION 2 - PHYSICAL/CHEMICAL CHARACTERISTICS |  |
| Boiling Point | 310 400o F | Specific Gravity (H2O = 1) |  |
| Vapor Pressure (mm Hg and Temperature) | 2 @ 68o F | Melting Point | N/A Liquid |
| Vapor Density (Air = 1) | Heavier | Evaporation Rate (Butyl Acetate = 1) | Slower |
| Solubility in Water | None | Water Reactive |  |
| Appearance and Odor Black fluid; odor characteristic of petroleum solvent |
| SECTION 3 - FIRE AND EXPLOSION HAZARD DATA |
| Flash Point and Method Used SETA 105o F | Auto-Ignition Temperature | Flammability Limits in Air % by Volume | LEL 0.9% | UEL 6.0% |
| Extinguisher Media Foam, CO2 Dry Chemical, Water Fog, Spray |
| Special Fire Fighting Procedures During emergency conditions, overexposure to decomposition products may cause a health hazard. Symptoms may not be immediately apparent. Obtain medical attention. |
| Unusual Fire and Explosion Hazards Do not mix or store with strong oxidants like liquid chlorine or oxygen. Keep containers tightly closed. Closed containers may explode when exposed to extreme heat. Application to hot surfaces requires special precautions. |

*  Optional	OSHA 174	Page 1/2	                                                                                          MSDS GAF

| SECTION 4 - REACTIVITY DATA |
| --- |
| STABILITY | Unstable ____ | Conditions to Avoid |
|  | Stable X |  |
| Incompatibility (Materials to Avoid): Strong Oxidants |
| Hazardous Decomposition Products: Fumes, Smoke and Carbon Monoxide if combustion is incomplete. |
| HAZARDOUS POLYMERIZATION | Conditions to Avoid |
| ____ May Occur X Will Not Occur |  |
| SECTION 5 – HEALTH HAZARD DATA |
| PRIMARY ROUTES OF ENTRY: | CARCINOGEN LISTED IN: |
| X Inhalation X Eyes X Skin X Ingestion | ___ NTP ___ IARC Monograph ___ OSHA ___ Not Listed |
| HEALTH HAZARDS | Acute and Chronic and Signs : Inhalation: Aspiration of material into the lungs can cause chemical pneumonitis which can be fatal. Ingestion: Swallowing can cause gastrointestinal irritation, nausea, vomiting, and diarrhea. Skin: Prolonged or repeated skin contact can cause moderate irritation or dermatitis. Eyes: Overexposure to vapors causes eye irritation, blurred vision, dizziness, headaches even unconsciousness. |
| EMERGENCY FIRST AID PROCEDURES: |
| Eye Contact: Flush with large amounts of water, lifting upper and lower lids occasionally. Get medical attention. |
| Skin Contact: Remove contaminated clothes and wash with waterless handcleaner and soap and warm water. |
| Inhalation: Remove from vapors immediately. If overcome, call a physician. If breathing stopped or irregular, start resuscitation or administer oxygen as needed. |
| Ingestion: Do not induce vomiting |
| SECTION 6 - CONTROL AND PROTECTIVE MEASURES |
| Respiratory Protection (Specify Type): Use hydrocarbon vapor canister or supplied air respiratory protection in confined or enclosed spaces—if needed. |
| Protective Gloves: Use chemical-resistant gloves if needed to avoid repeated or prolonged skin contact. | Eye Protection: Use splash goggles or face shield when eye contact may occur. |
| VENTILATION | ____ Local Exhaust: Face velocity 60fpm | _N/A___ Mechanical (General): |
| TO BE USED | ____ Special: Use only with adequate ventilation | ____ Other (Specify): N/A |
| Other Protective Clothing and Equipment: Use chemical-resistant apron or other clothing to a void repeated or prolonged skin contact. |
| Hygienic Work Practices: Use good hygiene when using all chemical products. |
| SECTION 7 – PRECAUTIONS FOR SAFE HANDLING AND USE/LEAK PROCEDURES |
| Steps to be Taken if Material is Spilled or Released: Remove sources of ignition. Keep people away. Recover free liquid. Add absorbent (sand, earth, sawdust, etc.) to spill area. Avoid breathing vapors. Ventilate confined spaces. Open all windows and doors. Keep products out of sewers and watercourses by diking or impounding, and advise authorities. |
| Waste Disposal Methods: Assure conformity with applicable disposal regulations. |
| Precautions to be Taken in Handling and Storage: Keep containers closed when not in use. Do not handle or store near heat, sparks, flame or strong oxidants. Adequate ventilation required. |
| Other Precautions and/or Special Hazards: Avoid breathing vapors. Avoid prolonged or repeated contact with skin. Remove contaminated clothing and launder before reuse. Remove contaminated shoes and thoroughly dry before reuse. Wash skin thoroughly with soap and water after contact. |

MSDS:  1014-U1                                                                                                                          Page 2/2