Concrete Products

Technical Guide Specification

Fiber Reinforcement For Concrete

SECTION 03240

PART 1 - GENERAL

1.01	SUMMARY

A.	This section specifies synthetic fiber reinforcement used as an admixture in concrete. Fibers shall serve as secondary reinforcement for concrete, and to protect concrete from stresses which cause cracking initially after placement.

B.	Related Sections: Other specification sections which directly relate to the work of this Section include, but are not limited to, the following:

1.	Section 03300 - Cast-In-Place Concrete.

2.	Section 03365 - Post-Tensioned Concrete.

3.	Section 03400 - Precast Concrete.

1.02	SUBMITTALS

A.	Product Data: Submit manufacturer’s product data, installation instructions, use limitations and recommendations for each material.

B.	Test and Performance Data: Submit independent test data substantiating compliance with ASTM C 1116 as specified.

1.03	QUALITY ASSURANCE

A.	Manufacturer: Fibers shall be manufactured by a firm with a minimum of 5 years experience in the production of similar products. Manufacturers proposed for use but not named in these specifications shall submit evidence of ability to meet all requirements specified, and include a list of projects of similar design and complexity completed within the past five years.

B.	Materials: For all admixtures required for the work of this Section, provide materials which are the products of one manufacturer.

C.	Pre-Construction Conference: A pre-installation conference shall be held two weeks prior to commencement of field operations to establish procedures to maintain optimum working conditions and to coordinate this work with related and adjacent work. Agenda for meeting shall include concrete and fiber handling, placing, finishing, and curing.

D.	Manufacturer’s Representative: A representative of the manufacturer shall be present for project start-up during initial concrete placement. Engineer may waive requirement for manufacturer’s representative if Contractor provides sufficient evidence that producer and finisher have adequate experience with fiber admixtures required.

1.04	PROJECT CONDITIONS

A.	Perform work only when existing and forecasted weather conditions are within the limits established by the manufacturer of the materials and products used.

PART 2 - PRODUCTS

2.01	MANUFACTURER

A.	Provide Grace MicroFiber™ concrete admixture by Grace Construction Products meeting specified requirements.  For customer service in North America:

Call toll free:		877-4AD-MIX1	(877-423-6491)

Fax toll free:		877-4AD-MIX2	(877-423-6492)

2.02	MATERIALS

A.	Fiber Reinforcement: Provide Grace MicroFiber concrete admixture by Grace Construction Products complying with the following requirements:

1.	Fibers: 1/2” or 3/4” (13 mm or 40 mm) polypropylene fibers, maximum 3 denier, complying with ASTM C 1116, Type III, Par. 4.1.3 and applicable building code requirements.

2.	Fibers Per Pound: Not less than 50 million individual fibers.

3.	Fibers shall be supplied in cellulose Concrete Ready Bags® which disperse during mixing.

2.03	CONCRETE MIX

A.	Application Rate: 1 pound per cubic yard (600 grams per cubic meter) of concrete unless recommended otherwise by the manufacturer. For uniform distribution, mix in truck for a minimum of 20 minutes after fiber addition. Add fibers at the batch plant to ensure proper mixing.

B.	Additional Concrete Admixtures: Additional concrete admixtures conforming to ASTM C 494 or equivalent CSA 266 standards may be used as required including the following.

1.	Type A: Water-reducing admixture, WRDA® series or Daracem®-55 by Grace Construction Products.

2.	Type D: Water-reducing and retarding admixture, Daratard-17 by Grace Construction Products.

3.	Type F or G: Water-reducing, high-range admixture, WRDA-19 or Daracem-100 by Grace Construction Products.

4.	Type C: Accelerating admixture, PolarSet® by Grace Construction Products.

5.	DCI® or DCI®-S Corrosion Inhibitor by Grace Construction Products may also be used if required at rate recommended by manufacturer.

PART 3 - EXECUTION

3.01	EXAMINATION

A.	Examine conditions of substrates and other conditions under which work is to be performed and notify Owner, in writing, of circumstances detrimental to the proper completion of the work. Do not proceed until unsatisfactory conditions are corrected.

3.02	CONCRETE PLACEMENT, FINISHING AND CURING

A.	Concrete Fibers: Comply with manufacturer’s recommendations for adding and mixing requirements.

B.	Concrete Finishing and Curing: Comply with ACI 302 “Guide for Concrete Floor and Slab Construction”, ACI 308 “Standard Practice for Curing Concrete”, ACI 305 “Hot Weather Concreting” and ACI 306 “Standard Practice for Cold Weather Concreting”. Finished concrete surface shall be a smooth surface with no exposed fibers.

3.03	PROTECTION

A.	Protect completed work from damage and construction operations throughout finishing and curing operations.

END OF SECTION

North American Customer Service: 1-877-4AD-MIX1 (1-877-423-6491)

Visit our website at: www.graceconstruction.com

W.R. Grace & Co.-Conn.	62 Whittemore Avenue	Cambridge, MA 02140	Tel: 617-876-1400

Daraccel, Daracem, Darapel, Daraset, Daratard, DCI, Force 10,000, PolarSet and WRDA are registered trademarks and MicroFiber is a trademark of W.R. Grace & Co.-Conn.

We hope the information here will be helpful.  It is based on data and knowledge considered to be true and accurate and is offered for the user’s consideration, investigation and verification, but we do not warrant the results to be obtained.  Please read all statements, recommendations or suggestions in conjunction with our conditions of sale which apply to all goods supplied by us.  No statement, recommendation or suggestion is intended for any use which would infringe any patent or copyright.  Grace Construction Products, W.R. Grace & Co.-Conn, 62 Whittemore Ave., Cambridge, MA  02140. In Canada, W.R. Grace & Co. Canada, Ltd. 294 Clements Road West, Ajax, Ontario, L1S 3C6.

© Copyright 2002. W.R. Grace & Co.-Conn.	Spec-3