Equipment Hatches - Guide Specifications

# SECTION 07 72 33            (1995 - 08316)

# PART 1: GENERAL

1.01    RELATED DOCUMENTS

A.     Conditions of the Contract and portions of Division One of this Project Manual apply to this Section as though repeated herein.

# 1.02    SUMMARY

Select one or more of the following subparagraphs as required by the Project.

A.     Section Includes:

1.      [Aluminum] [Galvanized Steel] Equipment Hatch.

2.      [Aluminum] [Galvanized Steel] Domed Equipment Hatch.

# 1.03    SUBMITTALS

A.  Product Data: For each type of equipment hatch indicated.  Include manufacturer's model number and accessories and requirements for roughing-in dimensions.

# 1.04    DELIVERY, STORAGE AND HANDLING

A.     Packing, Shipping, Handling and Unloading: Deliver equipment hatch as a factory assembled unit in manufacturer’s original packaging.

B.    Store materials in a dry, protected, well-vented area.  The contractor shall thoroughly inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

# PART 2: PRODUCTS

2.01    MANUFACTURER

A.   J L Industries, Incorporated

4450 West 78th Street Circle

### Bloomington, MN 55435

Telephone: (952) 835-6850/(800) 554-6077

FAX: (952) 837-1222

WEB: JLindustries.com

2.02    MANUFACTURED UNITS

A.  [Aluminum] [Galvanized Steel] Equipment Hatch.

Select one or more of the following for an equipment hatch size. If more than one size is required for the project, identify each type on a schedule located on the drawings and identify each type in the specification section. The first option for each model size is made from aluminum, the second option for each model size is made from galvanized steel.  Custom sizes are available.

1.   Model: [EHA-1] [EHG-1]; 72 inches by 96 inches clear opening.

2.   Model: [EHA-2] [EHG-2]; 72 inches by 120 inches clear opening.

3.   Model: [EHA-3] [EHG-3]; 120 inches by 120 inches clear opening.

4.   Model: [EHA-4] [EHG-4]; 144 inches by 144 inches clear opening.

5.   Characteristics:

a.   Curb and Curb Frame: [0.090 inch aluminum] [14 gauge galvanized steel], fully welded and ground smooth.

b.   Liner Metal: 22 gauge steel; ASTM A36/A36M.

c.   Curb Height: 12 inches.

d.   Lid Insulation: 1 inch fiberglass.

e.   Metal Finish: Factory primed.

f.    Hardware: Two-point universal spring latch, inside/outside handle with padlock provision, adjustable torsion springs, automatic hold-open and operating arms with red vinyl grip, and neoprene bulb seal.

A.  [Aluminum] [Galvanized Steel] Domed Equipment Hatch.

Select one or more of the following for a domed equipment hatch size. If more than one size is required for the project, identify each type on a schedule located on the drawings and identify each type in the specification section. The first option for each model size is made from aluminum, the second option for each model size is made from galvanized steel.  Custom sizes are available.

1.   Model: [DEHA-1] [DEHG-1]; 72 inches by 96 inches clear opening.

2.   Model: [DEHA-2] [DEHG-2]; 72 inches by 120 inches clear opening.

3.   Model: [DEHA-3] [DEHG-3]; 120 inches by 120 inches clear opening.

4.   Characteristics:

a.   Curb and Curb Frame: [0.090 inch aluminum] [14 gauge galvanized steel], fully welded and ground smooth.

b.   Liner Metal: 22 gauge steel; ASTM A36/A36M.

c.   Curb Height: 12 inches.

d.   Lid Insulation: 1 inch fiberglass.

e.   Metal Finish: Factory primed.

f.    Hardware: Two-point universal spring latch, inside/outside handle with padlock provision, adjustable torsion springs, automatic hold-open and operating arms with red vinyl grip, and neoprene bulb seal.

g.   Dome: One piece [clear] [translucent] acrylic dome.

# PART 3: EXECUTION

3.01    EXAMINATION

A.  Examine areas and conditions affecting installation.  Do not proceed with installation until unsatisfactory conditions have been corrected.

3.02    INSTALLATION

A.  Install system level and plumb, and in accord with manufacturer’s written instructions, original design and referenced standards.

# 3.03    ADJUSTING

A.  Adjust system for proper operation. Replace any parts that prevent the equipment hatch from operating properly.

3.04    CLEANING

A.  Remove all debris caused by installation of the equipment hatch. Clean all exposed surfaces to as fabricated condition and appearance.

3.05    PROTECTION

A.  Provide protection of the completed installation until completion of the project. Repair any damage at no additional cost.

3.06    SCHEDULES

If more than one type of equipment hatch is required, provide a schedule similar to the following example below. Use the corresponding type designations here and on the drawings,

A.     Type 1: [Describe by model].

B.    Type 2: [Describe by model].

C.    Type 3: [Describe by model