SHORT FORM SPECIFICATION

For assistance with detail review, contact Johns Manville Roofing Accessories Technical Services

1-800-445-1500, E-mail roofacc@jm.com  Website - www.jm.com

Roof Vent (FP-10  roof membrane vent- available as part of JM total roof system guarantee)

Warranty description for insertion into Part 1 of spec.   (Note:  Include the following where JM Single Ply,     Built-Up, or Modified Bitumen systems are specified to provide a total system guarantee.)

- Total System Guarantee:  Roof vent shall be included as part of the Johns Manville Roof System Guarantee.  See Section [       ].

Product description for insertion into Part 2 of spec.

- Roof Vent:  Johns Manville FP-10 One Way roof vent.

- Molded one piece [black polyethylene deck flange and body with weatherproof cap (Note: For built-up or modified bitumen systems)] [black ABS plastic resin deck flange and body with weatherproof gray ABS plastic resin cap (Note: For single ply systems)] and one way silicone rubber diaphragm that permits construction below roof membrane to breath.

Product installation for insertion into Part 3 of spec.

- Roof Vent:  Install roof drain and accessories in strict accordance with manufacturer’s written instructions, providing a permanent weather tight installation.

- Inspect and determine substrate to be in satisfactory condition.  All surfaces shall be smooth, dry, and clean.

- Locate vents [at locations indicated] [ uniformly across roof at a rate of {1} {__} vent(s) per 1000 square feet of roof area.

- Set flange in roof membrane compatible mastic and flash into roof system per roof vent and roof system manufacturer requirements.