SHORT FORM SPECIFICATION

For assistance with detail review, contact Johns Manville Roofing Accessories Technical Services

1-800-445-1500, E-mail - roofacc@jm.com  Website - www.jm.com

Roof Drain System (Flex-I-Drain roof drain with flexible bellows to allow differential movement between building system and piping - available as part of JM total roof system guarantee)

Warranty description for insertion into Part 1 of spec.   (Note:  Include the following where JM Single Ply,     Built-Up, or Modified Bitumen systems are specified to provide a total system guarantee.)

- Total System Guarantee:  Roof drain system shall be included as part of the Johns Manville Roof System Guarantee.  See Section [       ].

Product description for insertion into Part 2 of spec.

- Roof Drain System:  Johns Manville Flex-I-Drain.

- Rigid Components:  GE Noryl resin with high UV-resistance, tensile strength modulus, and heat deflection temperature resistance, meeting UL94V-1 requirements.

- Bellows:  Molded neoprene flexible boot attached to integral deck flange with no hub pipe connection.  Bellows shall allow differential movement up to one inch in any direction between the roof deck and piping.  Provide rubber adaptor bushings as required for pipe size.

- Strainer: 4 inch (102mm) high basket strainer.  Color [black (Note: Standard)] [white].  [Provide with 3 inch (76mm) high strainer extension.]

- Outlet Size: [3 inch (76mm)] [4 inch (102mm)] [5 inch (127mm)] [6 inch (152mm)].

Product installation for insertion into Part 3 of spec.

- Roof Drain System:  Install roof drain and accessories in strict accordance with manufacturer’s written instructions, providing a permanent weather tight installation.

- Inspect and determine substrate to be in satisfactory condition, with deck [and sump pan] fully anchored and aligned at proper location and elevation.  All surfaces shall be smooth, dry, clean, free of sharp edges, and other irregularities.

- Attach deck flange securely to substrate.

- Assemble and flash gravel stop flange into roof system per roof system and roof drain manufacturer requirements.

- Securely attach strainer basket.