SHORT FORM SPECIFICATION

For assistance with detail review, additional options, radius shapes and specialty one-of-a-kind products, contact Johns Manville Roofing Accessories Technical Services 1-800-445-1500,

E-mail - roofacc@jm.com  Website - www.jm.com

Roof Edge Strip (Presto Stop one piece direct nail edge strip with continuous cleat  - available as part of JM total roof system guarantee)

Warranty description for insertion into Part 1 of spec.   (Note:  Include the following where JM Single Ply,     Built-Up, or Modified Bitumen systems are specified to provide a total system guarantee.)

- Total System Guarantee:  Roof edge strip shall be included as part of the Johns Manville Roof System Guarantee.  See Section [       ].

Product description for insertion into Part 2 of spec.

- Roof Edge Strip:  Johns Manville Presto Stop.

- Edge Strip:  10 feet ( 3m) long, with matching concealed splice plate,  [ ___inch ( ___mm)] face width .  (Note: Special size and shapes available, contact JM.)

- Metal: [{.050 inch (1.3mm)} {.040 inch (.91mm)} thick aluminum in {mill} {clear anodized} {color anodized} {Kynar 500} finish.]  [{22 gage (.9mm)} {24 gage (.7mm)} galvanized steel with Kynar 500 finish] [Color {as indicated} { selected by Architect from manufacturer’s standard colors}.]  (Note:  Other metals, colors and finishes available,  contact JM.)

- Cleat:  24 gage (.7mm) galvanized steel, continuous.

- Extender Plate:  Same metal, gage and finish as edge strip.  Continuous 24 gage (.7mm) galvanized steel concealed connector clip for securing bottom edge.

- Accessories:  [Scupper] and [sump with collector box and outlet of required shape and size].  Same metal, gage and finish as edge strip.

- Fasteners:   Minimum 1-1/2 inch (38mm) long hot-dipped galvanized roofing nails.

Product installation for insertion into Part 3 of spec.

- Roof Edge Strip:  Install edge strip and accessories in strict accordance with manufacturer’s written instructions, providing a permanent weather tight installation.

- Inspect and determine substrate to be in satisfactory condition, with pressure treated blocking fully anchored and aligned at proper location and elevation.  All surfaces shall be smooth, dry, clean, free of splinters, sharp edges, and other irregularities.

- Fasten continuous cleat to wood blocking at 8 inches (203mm) on center.  Nail flange to wood blocking at 4 inches (101mm) on center, providing 1/2 inch (13mm) between sections.  Provide 5 inch (127mm) wide splice plate at each joint.

- Flash flanges into roof system per roof system manufacturer requirements.

Remove protective film from covers immediately after installation.