PART 1	GENERAL

1.1	SUMMARY

A.	Section includes:  Provide a complete polyurethane waterproofing coating system where indicated on the Drawings, including all applicable sealants and elastomeric flashings needed to ensure a complete waterproof and weathertight system for deck, ramp, stair and landing surfaces at locations indicated.

B.	Related work:

1.	Documents affecting work of this Section include, but are not necessarily limited to, General Conditions, Supplementary Conditions, and Sections in Division 1 of these Specifications.

1.2	SUBMITTALS

A.	Comply with pertinent provisions of Section 01340.

B.	Product data:

1.	Materials list of items proposed to be provided under this Section;

2.	Manufacturer's specifications and other data needed to prove compliance with the specified requirements;

3.	Shop Drawings or catalog illustrations in sufficient detail to show installation and interface of the work of this Section with the work of adjacent trades;

4.	Manufacturer's current recommended installation procedures which, when approved by the Architect, will become the basis for accepting or rejecting actual installation procedures used on the Work.

5.	Written documentation of applicator's qualifications, including reference projects of similar scope and complexity, with current phone contacts of architects and owners for verification.

1.3	QUALITY ASSURANCE

A.	Use adequate numbers of skilled workmen thoroughly trained and experienced in the necessary crafts and completely familiar with the specified requirements and methods needed for proper performance of the work of this Section.

B.	Applicator qualifications:

1.	Applicator shall have at least three years experience in installing materials of types specified and shall have successfully completed at least three projects of similar scope and complexity.

2.	Applicator shall designate a single individual as project foreman who shall be on site at all times during installation.

C.	Convene a pre-installation job-site conference four weeks prior to commencing work of this Section:

1.	Secure attendance by Architect, Contractor, applicator, and authorized representatives of the coating system manufacturer and interfacing trades.

2.	Examine Drawings and Specifications affecting work of this Section, verify all conditions, review installation procedures, and coordinate scheduling with interfacing portions of the Work.

1.4	DELIVERY, STORAGE AND HANDLING

A.	Deliver materials to job site in manufacturer's unopened containers with all labels intact and legible at time of use.

B.	Maintain the products in accord with manufacturer's recommendations with proper precautions to ensure fitness of material when installed.

C.	Comply with pertinent provisions of Section 01620.

1.5	SUBSTRATE CONDITIONS

A.	General:

1.	Provide applicator with surfaces that are broom clean, dry, sound and free of voids, bugholes, rockpockets, honeycombs, protrusions, excessive roughness, foreign matter, frost, ice and other contaminants which may inhibit application or performance of the waterproofing coating system.

2.	Using suitable abrasive methods, remove residue of form release, curing compound, chemical retarders and other surface treatments, laitance, mortar smear, sawcutting residue, mill scale, rust, loose material and other contaminants from concrete, masonry and ferrous metal surfaces to receive the work of this Section.

B.	Concrete:  Where work of this Section will be applied to concrete, provide surfaces that are smooth with finish equal to one that is light steel troweled followed by a fine hair broom.

C.	Decks:

1.	Slope deck surfaces to drains that have flanges at coating level which are flush with deck surfaces.

2.	Rigidly install pipe, vents and other surface protrusions, properly flash them, and cover to prevent entry of coating materials.

D.	Metal flashings:  Where metal flashings are substrate to waterproofing coating, set the flashings in continuous bedding bead of urethane sealant; install sealant S-bead between metal laps and mechanically fasten to substrate along leading edges at every 4" on center, staggered linearly, to lay flat without fishmouths.

E.	Joints:  Configuration shall be consistent with this Section and with all other requirements of the Contract Documents.

1.6	WARRANTY

A.	Deliver to the Architect signed copies of the following written warranties against defective materials and workmanship for a period of one year following date of completion.  Warrant that installed waterproof coating system shall be free of defects including adhesive failure, cohesive failure, weathering deficiencies and waterproofing failure resulting from substrate cracking up to 1/16 inch.

1.	Manufacturer's standard warranty covering materials;

2.	Applicator's standard warranty covering workmanship.

PART 2	PRODUCTS

2.1	GENERAL

A.	Provide a complete "“Vulkem 360NF/951NF” liquid applied polyurethane waterproofing coating system manufactured by Tremco Inc. (800) 852 -8173 and having the following minimum attributes:

1.	System designed for continuously immersed conditions;

2.	Complying with ASTM C957-91 and having a Class A fire rating on concrete substrates.

3.	Color to be selected by Architect from manufacturer's standard color range.

2.2	ACCESSORIES

A.	Primer:  As recommended by coating system manufacturer.

B.	Joint backing:  Closed-cell, polyethylene rod as recommended by coating manufacturer.

C.	Sealant:  As recommended by coating manufacturer.  Vulkem 116 or Dymeric 240FC.

2.3	OTHER MATERIALS

A.	Provide other materials, not specifically described but required for a complete and proper installation, as selected by the Contractor and approved by the coating system manufacturer as compatible, subject to the approval of the Architect.

PART 3	EXECUTION

3.1	SURFACE CONDITIONS

A.	Coordinate as required with other trades to assure proper and adequate provision in the work of those trades for interface with the work of this Section.

B.	Applicator shall examine the areas and conditions under which work of this Section will be performed.

1.	Verify conformance with manufacturer's requirements;

2.	Report unsatisfactory conditions in writing to the Architect;

3.	Do not proceed until unsatisfactory conditions are corrected.

3.2	PREPARATION

A.	Surface preparation and detailing procedures to be in accord with waterproof coating system manufacturer's instructions and recommendations except where more stringent requirements are indicated.

B.	Clean all deck surfaces to receive coating system in accord with manufacturer's instructions;  vacuum clean or blow clean with oil-free compressed air all surfaces to receive sealants, detailing materials or coatings immediately prior to installation.

C.	Rout, clean, prepare and detail surface cracks in accord with manufacturer's instructions;  install backer rod where required.

D.	Clean metal surfaces to bright metal by wire brushing or mechanical etching;  scuff-sand lead flashing and plastic surfaces.

E.	Prime surfaces in accord with manufacturer's instructions only as required or recommended by the manufacturer.

F.	Install 1/4" diameter backer rod into corner of all horizontal-to-vertical junctures subject to movement and cover with 1" detail cant of approved sealant;  install 1" detail cants at projections, curbs and other horizontal-to-vertical junctures.

G.	Install detail coats, joint and crack treatments, and liquid flashings in accord with manufacturer's instructions.

H.	Allow detail applications to cure in accord with manufacturer's instructions prior to general application of coating.

3.3	APPLICATION

A.	Install waterproof coating system in accord with manufacturer's recommendations and instructions as applies to the Work except where more stringent requirements are indicated.

1.	Grid deck surfaces to assure proper coverage rates and verify coating wet-film mil thickness with gauges as work progresses.

2.	Retain empty product containers during course of work to aid in determining whether completed coating system complies with manufacturers average thickness requirements.

3. 1   Apply Vulkem 360NF, 60 mils (1.0mm) thick to the entire area to be coated, including over all detail coats, but excluding expansion joints. The most popular method of application is with a notched squeegee. Backroll to evenly distribute coating and to eliminate pinholes. Vulkem 360NF-SL can also be applied with a roller equipped with a solvent resistant roller sleeve.

3.2   Allow Vulkem 360NF to cure a minimum of 6 hours and a maximum of 24 hours at 75°F 	(24°C), 50% relative humidity.

3.3   When a fast cure time is desirable, Vulkem 360NF Quick Cure Catalyst can be added after the water has been added and mixed into the system. The Vulkem 360NF Quick Cure Catalyst   will enable the applicator to topcoat the system within 3 hours at 75°F (24°C), 50% relative humidity.

Note: Vulkem 360NF should have a slightly tacky surface to aid in the adhesion of the Vulkem 951NF. If the membrane coat has reached a tack-free cure, the surface must be cleaned with a cloth that has been wet with Xylol (Xylene).

DO NOT SATURATE THE SURFACE WITH SOLVENT. IF THE VULKEM MEMBRANE COAT HAS BEEN ALLOWED TO BE EXPOSED FOR A PROLONGED PERIOD, IT SHOULD BE CLEANED, THEN PRIME COATED WITH EITHER VULKEM PRIMER 191 OR TREMPRIME MULTI-SURFACE URETHANE PRIMER.

3.4   After the base coat has been installed and allowed to cure, install a layer of the Vulkem 951NFat a rate of 100-150 square feet per gallon, using a short (1/4”) solvent-resistant nap roller.

3.5   The first coat of Vulkem 951NF should be allowed to cure for 8-12 hours (at 70°F). Install a second coat of Vulkem 951NF. Let this layer cure.

  - Clean all adjacent areas, tools or equipment to remove any stains or spills with MEK, Toluene

or Xylene.

4.2   Clean hands by soaking in hot, soapy water then brush with a stiff bristle brush.

END OF SECTION