VersiWeld

Mechanically Attached

Form-Spec

January, 2007

Note to the User:  Some text has been colored and underlined so the specifier can customize a specification for a specific project.  This information must be edited by the specifier to create a final draft of the project specification.  Page breaks should also be checked to maximize page usage once specific project information has been added by the specifier.

PART 1	GENERAL

1.01	DESCRIPTION

A.	The (Project Name) is located at (Address) in (City and State).  (Name of Project Manager), Project Manager/Coordinator, is the Owner's Representative and may be contacted regarding any questions or for a pre-bid job site inspection, phone (Phone Number).

B.	The project consists of installing Versico's VersiWeld (TPO) Mechanically Attached Roofing System as outlined below: :  (choose the appropriate paragraph and delete remainder)

Apply the VersiWeld Mechanically Attached Roofing System in conjunction with (Insulation Type) over the new (Deck Type) roof deck.

OR

Apply the VersiWeld Mechanically Attached Roofing System in conjunction with (Insulation Type) over the existing (Material Type) roof.

OR

Apply the VersiWeld Mechanically Attached Roofing System in conjunction with (Insulation Type) after tear off of the existing (Material Type) roof to expose the (Roof Deck Type) for verification of suitable substrate as specified in this specification.

1.02	EXTENT OF WORK

A.	Provide all labor, material, tools, equipment, and supervision necessary to complete the installation of the VersiWeld (.045”, .060”, .072” or .080”) thick (white, gray or tan) reinforced TPO (Thermoplastic Polyolefin) membrane Mechanically Attached Roofing System including flashings and insulation as specified herein and as indicated on the drawings in accordance with the manufacturer's most current specifications and details.

B.	The roofing contractor shall be fully knowledgeable of all requirements of the contract documents and shall make themselves aware of all job site conditions that will affect their work.

C.	The roofing contractor shall confirm all given information and advise the building owner, prior to bid, of any conflicts that will affect their cost proposal.

D.	Any contractor who intends to submit a bid using a roofing system other than the approved manufacturer must submit for pre-qualification in writing fourteen (14) days prior to the bid date.  Any contractor who fails to submit all information as requested will be subject to rejection.  Bids stating "as per plans and specs" will be unacceptable.

1.03	SUBMITTALS

A.	Prior to starting work, the roofing contractor must submit the following:

1.	Shop drawings showing layout, details of construction and identification of materials.

2.	Sample of the manufacturer's Membrane System Warranty.

3.	Submit a letter of certification from the manufacturer which certifies the roofing contractor is authorized to install the manufacturer's roofing system and lists foremen who have received training from the manufacturer along with the dates training was received.

- Certification from the membrane manufacturer indicating the fasteners are capable of providing a static backout resistance of 10 inch pounds minimum is required.

- Certification from the membrane manufacturer indicating the membrane thickness over the reinforcing scrim (top ply membrane thickness) is nominal .015” (15 mil).

- Certification of the manufacturer's warranty reserve.

B.	Upon completion of the installed work, submit copies of the manufacturer's final inspection to the specifier prior to the issuance of the manufacturer's warranty.

1.04	PRODUCT DELIVERY, STORAGE AND HANDLING

A.	Deliver materials to the job site in the manufacturer's original, unopened containers or wrappings with the manufacturer's name, brand name and installation instructions intact and legible.  Deliver in sufficient quantity to permit work to continue without interruption.

B.	Comply with the manufacturer's written instructions for proper material storage.

1.	Store VersiWeld membrane in the original undisturbed plastic wrap in a cool, shaded area and cover with light-colored, breathable, waterproof tarpaulins.  VersiWeld membrane that has been exposed to the elements for approximately 7 days must be prepared with Versico Weathered Membrane Cleaner prior to hot air welding.

2.	Store curable materials (adhesives and sealants) between 60F and 80F in dry areas protected from water and direct sunlight.  If exposed to lower temperature, restore to 60F minimum temperature before using.

3.	Store materials containing solvents in dry, well ventilated spaces with proper fire and safety precautions.  Keep lids on tight.  Use before expiration of their shelf life.

C.	Insulation must be on pallets, off the ground and tightly covered with waterproof materials.

D.	Any materials which are found to be damaged shall be removed and replaced at the Contractor's expense.

1.05	WORK SEQUENCE

A.	Schedule and execute work to prevent leaks and excessive traffic on completed roof sections.  Care should be exercised to provide protection for the interior of the building and to ensure water does not flow beneath any completed sections of the membrane system.

- Do not disrupt activities in occupied spaces.

  - USE OF THE PREMISES

A.	Before beginning work, the roofing contractor must secure approval from the building owner's representative for the following:

1.	Areas permitted for personnel parking.

2.	Access to the site.

3.	Areas permitted for storage of materials and debris.

4.	Areas permitted for the location of cranes, hoists and chutes for loading and unloading materials to and from the roof.

B.	Interior stairs or elevators may not be used for removing debris or delivering materials, except as authorized by the building superintendent.

1.07	EXISTING CONDITIONS

If discrepancies are discovered between the existing conditions and those noted on the drawings, immediately notify the owner's representative by phone and solicit the manufacturer's approval prior to commencing with the work.  Necessary steps shall be taken to make the building watertight until the discrepancies are resolved.

1.08	PRE-CONSTRUCTION CONFERENCE

A.	A pre-bid meeting will be held at the job site on (Date) at (Time).  Contact the owner's representative, (Name and Title), at (Phone Number) if there are any questions.

B.	Prior to bid submittal, the roofing contractor should schedule a job site inspection to observe actual conditions and verify all dimensions on the roof.  The job site inspection may occur on the day of the pre-bid meeting or prior to such a meeting.  Should access to the roof be necessary before or after the pre-bid meeting, the contractor must contact the owner's representative, (Name and Title), at (Phone Number) to coordinate an appropriate time.

C.	Bids must be forwarded to the following address no later than (Time) on (Date):

(Name and Address)

D.	Any conditions which are not shown on the shop drawings should be indicated on a copy of the shop drawing and included with bid submittal if necessary to clarify any conditions not shown.

1.09	TEMPORARY FACILITIES AND CONTROLS

A.	Temporary Utilities:

1.	Water, power for construction purposes and lighting (are/are not) available at the site and (will/will not) be made available to the roofing contractor.

2.	Provide all hoses, valves and connections for water from source designated by the owner when made available.

3.	When available, electrical power should be extended as required from the source.  Provide all trailers, connections and fused disconnects.

B.	Temporary Sanitary Facilities

Sanitary facilities will not be available at the job site.  The roofing contractor shall be responsible for the provision and maintenance of portable toilets or their equal.

C.	Building Site:

1.	The roofing contractor shall use reasonable care and responsibility to protect the building and site against damages.  The contractor shall be responsible for the correction of any damage incurred as a result of the performance of the contract.

2.	The roofing contractor shall remove all debris from the job site in a timely and legally acceptable manner so as to not detract from the aesthetics or the functions of the building.

D.	Security:

Obey the owner's requirements for personnel identification, inspection and other security measures.

1.10	JOB SITE PROTECTION

A.	The roofing contractor shall adequately protect building, paved areas, service drives, lawn, shrubs, trees, etc. from damage while performing the required work.  Provide canvas, boards and sheet metal (properly secured) as necessary for protection and remove protection material at completion.  The contractor shall repair or be responsible for costs to repair all property damaged during the roofing application.

B.	During the roofing contractor's performance of the work, the building owner will continue to occupy the existing building.  The contractor shall take precautions to prevent the spread of dust and debris, particularly where such material may sift into the building.  The roofing contractor shall provide labor and materials to construct, maintain and remove necessary temporary enclosures to prevent dust or debris in the construction area(s) from entering the remainder of the building.

C.	Do not overload any portion of the building, either by use of or placement of equipment, storage of debris, or storage of materials.

D.	Protect against fire and flame spread.  Maintain proper and adequate fire extinguishers.

E.	Take precautions to prevent drains from clogging during the roofing application.  Remove debris at the completion of each day's work and clean drains, if required.  At completion, test drains to ensure the system is free running and drains are watertight.  Remove strainers and plug drains in areas where work is in progress.  Install flags or other telltales on plugs.  Remove plugs each night and screen drain.

F.	Store moisture susceptible materials above ground and protect with waterproof coverings.

G.	Remove all traces of piled bulk materials and return the job site to its original condition upon completion of the work.

1.11	SAFETY

The roofing contractor shall be responsible for all means and methods as they relate to safety and shall comply with all applicable local, state and federal requirements that are safety related.  Safety shall be the responsibility of the roofing contractor.  All related personnel shall be instructed daily to be mindful of the full time requirement to maintain a safe environment for the facility's occupants including staff, visitors, customers and the occurrence of the general public on or near the site.

1.12	WORKMANSHIP

A.	Contractors installing new roof, flashing and related work shall be factory trained and approved by the manufacturer they are representing.

B.	All work shall be of highest quality and in strict accordance with the manufacturer's published specifications and to the building owner's satisfaction.

C.	There shall be a supervisor on the job site at all times while work is in progress.

  - QUALITY ASSURANCE

A.	The VersiWeld membrane roofing system must achieve a UL Class (A, B or C) and/or FM (1-60, 1-75, 1-90, 1-105, 1-120 or 1-135) rating.

B.	Unless otherwise noted in this specification, the roofing contractor must strictly comply with the manufacturer's current specifications and details.

C.	The roofing system must be installed by a contractor authorized and trained by the manufacturer in compliance with shop drawings as approved by the manufacturer.

D.	Provide adequate number of experienced workmen regularly engaged in this type of work who are skilled in the application techniques of the materials specified.  Provide at least one thoroughly trained and experienced superintendent on the job at all times roofing work is in progress.

E.	There shall be no deviations made from this specification or the approved shop drawings without the prior written approval of the specifier.  Any deviation from the manufacturer's installation procedures must be supported by a written certification on the manufacturer's letterhead and presented for the specifier's consideration.

F.	Upon completion of the installation, the Contractor shall arrange for an inspection to be made by a non-sales technical representative of the membrane manufacturer in order to determine whether or not corrective work will be required before the warranty will be issued.  Notify the building owner seventy-two (72) hours prior to the manufacturer's final inspection.

1.14	JOB CONDITIONS, CAUTIONS AND WARNINGS

Refer to Versico's VersiWeld Mechanically Attached Roofing System specification, Part II - Application, for General Job Site Considerations.

A.	Material Safety Data Sheets (MSDS) must be on location at all times during the transportation, storage and application of materials.

B.	When positioning membrane sheets, exercise care to locate all field splices away from low spots and out of drain sumps.  All field splices should be shingled to prevent bucking of water.

C.	When loading materials onto the roof, the Versico Authorized Roofing Contractor must comply with the requirements of the building owner to prevent overloading and possible disturbance to the building structure.

D.	Proceed with roofing work only when weather conditions are in compliance with the manufacturer's recommended limitations, and when conditions will permit the work to proceed in accordance with the manufacturer's requirements and recommendations.

E.	Proceed with work so new roofing materials are not subject to construction traffic.  When necessary, new roof sections shall be protected and inspected upon completion for possible damage.

F.	Provide protection, such as 3/4 inch thick plywood, for all roof areas exposed to traffic during construction.  Plywood must be smooth and free of fasteners and splinters.

G.	The surface on which the insulation or roofing membrane is to be applied shall be clean, smooth, dry, and free of projections or contaminants that would prevent proper application of or be incompatible with the new installation, such as fins, sharp edges, foreign materials, oil and grease.

H.	New roofing shall be complete and weathertight at the end of the work day.

I.	Contaminants such as grease, fats and oils shall not be allowed to come in direct contact with the roofing membrane.

1.15	WARRANTY

A.	Provide manufacturer's (5 year / 10 year) Membrane System Warranty covering both labor and material with no dollar limitation.  The maximum wind speed coverage shall be peak gusts of 55 mph measured at 10 meters above ground level.

OR

Provide manufacturer's (10 year / 15 year) Total System Warranty covering both labor and material with no dollar limitation.  The maximum wind speed coverage shall be peak gusts of (55, 72, 80, 90 or 100 mph) measured at 10 meters above ground level.  Certification is required with bid submittal indicating the manufacturer has reviewed and agreed to such wind coverage.

OR

Provide manufacturer's 20 year Total System Warranty covering both labor and material with no dollar limitation.  The maximum wind speed coverage shall be peak gusts of (55, 72 or 90 mph) measured at 10 meters above ground level.  Certification is required with bid submittal indicating the manufacturer has reviewed and agreed to such wind coverage.

[Note:	When .072” or .080” thick VersiWeld Plus membrane is specified, a warranty covering leaks caused by accidental punctures, up to 16 man-hours per year, is available.]

[Note:	When minimum .045” thick white VersiWeld membrane is specified, a Reflectivity Warranty Amendment is available indicating the membrane will meet the Energy Star program reflectivity guidelines for both new and aged membrane for a period of 10 years.]

B.	Pro-rated System Warranties shall not be accepted.

C.	Evidence of the manufacturer's warranty reserve shall be included as part of the project submittals for the specifier's approval.

PART 2	PRODUCTS

2.01	GENERAL

A.	All components of the specified roofing system shall be products of Versico Incorporated or accepted by Versico as compatible.

B.	All products (including insulation, fasteners, fastening plates and edgings) must be manufactured and supplied by the roofing system manufacturer and covered by the warranty.

2.02	MEMBRANE

Furnish VersiWeld (.045”, .060”, .072” or .080”) thick (white, gray or tan) reinforced TPO (Thermoplastic Polyolefin) membrane as needed to complete the roofing system.  Membrane thickness over the reinforcing scrim (top-ply thickness) shall be nominal .015” thick (15 mil).

2.03	INSULATION/UNDERLAYMENT

A.	When applicable, insulation shall be installed in multiple layers.  The first and second layer of insulation shall be mechanically attached to the substrate in accordance with the manufacturer's published specifications.

B.	Insulation shall be Versico (Type of Insulation) as supplied by Versico.  Minimum R-value required is (Note R-Value).

2.04	ADHESIVES AND CLEANERS

All products shall be furnished by Versico and specifically formulated for the intended purpose.

A.	Bonding Adhesive:  VersiWeld

B.	Edge Sealant: Cut Edge Sealant

- Sealer: Water Cut-Off Mastic and PT 304 Sealant

- Pocket Sealant:  TPO Molded Pocket Sealant

E.	Cleaner:  Versico Weathered Membrane Cleaner

2.05	FASTENERS AND PLATES

To be used for mechanical attachment of insulation and to provide additional membrane securement: (delete the fastener and fastening plate types which will not be used)

- HPVX Fasteners: A heavy duty #15 threaded fastener with a phillips head used for membrane securement into steel, wood plank or minimum 15/32 inch thick plywood.

- HPV-XL Fasteners:  An oversized diameter (.315”) steel threaded fastenerused in conjunction with Piranha Xtra Plates for membrane securement into steel or wood decks.

- HPV Fasteners:  A threaded, black epoxy electro-deposition coated fastener used with steel and wood roof decks for insulation attachment only.

- Pre-Assembled ASAP Fasteners:  A pre-assembled 3” diameter Plastic Plate and standard phillips head fastener used for insulation attachment only into steel or wood decks.  Installed using Olympic Fastening Tools.

- InsulFast Fasteners:  A threaded #12 fastener with #3 phillips head used for insulation attachment only into steel or wood decks.

- CD-10 Fasteners:  A non-threaded, hammer driven fastener used with structural concrete roof decks rated 3,000 psi or greater.

- MP-14-10 Fasteners: A #14 threaded fastener used for minimum 3,000 psi concrete decks.

- NTB Fasteners:  A non-penetrating, plastic fastener and corresponding plate used with lightweight deck substrates such as cementitious wood fiber, gypsum, and lightweight insulating concrete.

- HP Term Bar Nail-Ins:  A 1-1/4” long expansion anchor with a zinc plated steel drive pin used for fastening the Versico Termination Bar or Seam Fastening Plates to concrete, brick, or block walls.

- HPVX Fasteners: A 2-3/8 inch diameter metal barbed fastening plate used with Versico Fasteners for membrane securement.  This plate can be used for insulation securement.

- HPV-XL Plates: A 2-3/8 inch diameter metal barbed fastening plate with an oversized hole for use with Versico HPVX Fasteners for membrane securement.  This plate can be used for insulation securement.

- Insulation Fastening Plates:  a nominal 3 inch diameter metal plate used for insulation attachment with the appropriate Versico Fastener.

2.06	METAL EDGING AND MEMBRANE TERMINATIONS

(Choose the appropriate type of metal edging or membrane termination and delete the types which will not be used)

- Versico VersiTrim 2000:  a metal fascia system with a heavy duty .100” thick extruded aluminum anchor bar and .040 inch thick aluminum or 24 gauge steel fascia.  Metal fascia color shall be as designated by the Owner's Representative.

- VersiTrim 1000:  A metal anchor bar fascia system consisting of a formed quarter hard 0.050” aluminum retainer bar, corrosion resistant fasteners and a 0.040” aluminum or 24 gauge steel snap-on fascia cover.   Metal fascia color shall be as designated by the Owner's Representative.

- VersiTrim 3000:  A metal anchor bar fascia system consisting of a 20 gauge steel retainer bar, corrosion resistant fasteners and an aluminum or 24 gauge steel snap-on fascia cover.  Metal fascia color shall be as designated by the Owner's Representative.

- Versico VersiTrim: a snap-on edge system consisting of a 26 gauge galvanized metal water dam and .050 inch thick aluminum or 24 gauge galvanized steel fascia.  Metal fascia color shall be as designated by the Owner's Representative.

- Versico VersiTrim 200: a snap-on edge system consisting of a 24 gauge galvanized metal water dam and .040”, .050” or .063” thick Kynar 500, clear and colored anodized finish or 24 gauge steel, Kynar 500 finish.  Metal fascia color shall be as designated by the Owner's Representative.

- VersiTrim 1 Piece Gravel Stop:  a 22 gauge, 12 foot long, pre-punched 90 degree angle cleat and 12 foot long fascia section.  Available in .040”, .050” or .063” thick Kynar 500, clear and colored anodized finish or 24 gauge steel, Kynar 500 finish.  Metal fascia color shall be as designated by the Owner's Representative.

- Versico Drip Edge:  a metal fascia/edge system with a 22 or 24 gauge continuous anchor cleat and .032 inch thick aluminum or 24 gauge steel fascia.  Metal fascia color shall be as designated by the Owner's Representative.

- VersiWeld Coated Metal: 4'x 10' coated metal sheeets made from 24 gauge galvanized steel with a minimum .035" thick non-reinforced (white, gray or tan) VersiWeld laminate.  VersiWeld membrane can be welded directly to the VersiWeld Coated Metal in accordance with the manufacturer’s detail.

- Versico VersiTrim Coping:  incorporates a 20 gauge anchor cleat with 4 pre-slotted holes, a concealed joint cover and 10 foot continuous sections of coping cap; can accommodate minimum 5 inch wide parapet walls.  Metal coping cap color shall be as designated by the Owner's Representative.

- Versico Termination Bar:  a 1 inch wide and .098 inch thick extruded aluminum bar pre-punched 6 inches on center; incorporates a sealant ledge to support Lap Sealant and provide increased stability for membrane terminations.

2.07	OTHER MATERIALS

(Metal Flashing, if required, and miscellaneous items needed to fulfill the project requirements)

PART 3	EXECUTION

3.01	GENERAL

A.	Comply with the manufacturer's published instructions for the installation of the membrane roofing system including proper substrate preparation, jobsite considerations and weather restrictions.

B.	Position sheets to accommodate contours of the roof deck and shingle splices to avoid bucking water.

3.02	INSULATION PLACEMENT AND ATTACHMENT

A.	Install insulation or membrane underlayment over the substrate with boards butted tightly together with no joints or gaps greater than 1/4 inch.  Stagger joints both horizontally and vertically if multiple layers are provided.

B.	Secure insulation to the substrate with the required Versico fasteners and plates in accordance with manufacturers specifications.

3.03	MEMBRANE PLACEMENT AND ATTACHMENT

A.	Unroll and position membrane without stretching.  Provide and secure both perimeter and field membrane sheets in accordance with the manufacturer's most current specifications and details.

B.	Secure the membrane with the required Versico Fasteners and Plates spaced a maximum of 12 inches on center depending or project conditions (centered over the pre-printed marks approximately 1-1/2 inches from the edge of the membrane sheet).

C.	Install adjoining membrane sheets in the same manner in accordance with the manufacturer's specifications.

3.04	MEMBRANE SPLICING/HOT AIR WELDING PROCEDURES

A.	Hot air weld the VersiWeld membrane using an Automatic Hot Air Welding Machine or Hot Air Hand Welder in accordance with the manufacturer's specifications.  At all splice intersections, roll the seam with a silicone roller prior to membrane seam cooling.  (Note:  When using .060” thick membrane, all splice intersections shall be overlaid with VersiWeld non-reinforced flashing)

B.	Probe all seams once the hot air welds have thoroughly cooled (approximately 30 minutes).

C.	Repair all seam deficiencies the same day they are discovered.

D.	Apply Cut Edge Sealant on all cut edges of reinforced membrane (where the scrim reinforcement is exposed) after seam probing is complete.

3.05	FLASHING

A.	Flashing of parapets, curbs, expansion joints and other parts of the roof must be performed using VersiWeld reinforced membrane.  VersiWeld non-reinforced membrane can be used for flashing pipe penetrations, Sealant Pockets, scuppers, as well as inside and outside corners when the use of pre-fabricated accessories is not feasible.

B.	Follow manufacturer's typical flashing procedures for all wall, curb, and penetration flashing including metal edging/coping and roof drain applications.

3.06	WALKWAYS

A.	Install walkways at all traffic concentration points (such as roof hatches, access doors, rooftop ladders, etc.) and all locations as identified on the specifier's drawing.

B.	(Hot air weld walkway pads to the membrane or install concrete pavers, loose laid over an approved protection sheet) in accordance with the manufacturer's specifications.

3.07	DAILY SEAL

A.	On phased roofing, when the completion of flashings and terminations is not achieved by the end of the work day, a daily seal must be performed to temporarily close the membrane to prevent water infiltration.

B.	Complete an acceptable membrane seal in accordance with the manufacturer's requirements.

3.08	CLEAN UP

A.	Perform daily clean-up to collect all wrappings, empty containers, paper, and other debris from the project site.  Upon completion, all debris must be disposed of in a legally acceptable manner.

B.	Prior to the manufacturer's inspection for warranty, the Contractor must perform a pre-inspection to review all work and to verify all flashing has been completed as well as the application of all caulking.

END OF SPECIFICATION